## Slide 1: Aeromedical Factors

## Slide 2: Introduction
Drugs
Alcohol
Fatigue and dehydration
Hypoxia
Hyperventilation
Ear and sinus problems
Spatial disorientation
Vision and effective visual scanning
Flight after SCUBA diving
Personal medical checklist
Summary of aeromedical factors can be found in AIM Ch. 8

## Slide 3: Motivation
Glider Flying=No FAA medical required
HOWEVER, exercising the privileges of your glider pilot’s license requires that you certify that you have no known medical deficiencies that would hamper your ability to fly
Also, for the safety and comfort of your passengers, knowledge of aeromedical factors is required
Finally, knowledge of this topic is required during your practical test

## Slide 4: Drugs
FAR 91.17 prohibits the pilot from flying “While using any drug that affects the person's faculties in any way contrary to safety”
Both some prescription drugs as well as many common over-the-counter drugs may compromise safety
Tranquilizers, antihistamines, sedatives, strong pain relievers, and cough suppressants may impair judgment, memory, alertness, coordination, vision, and decision-making
The effects of many drugs may be intensified or altered at altitude…don’t assume because you feel OK on the ground you will be OK in flight
In particular, sedatives, transquilizers, and antihistamines increase susceptibility to hypoxia

## Slide 5: Alcohol
FAR 91.17 contains specific prohibitions against flying while under the influence of alcohol
You CAN be under the influence of alcohol, despite being in compliance with specific provisions of 91.17 (i.e. more than 8-hours after drinking and < 0.04% BAC)
  For example, if you’re hung over 10 hours after drinking, you’re still “under the influence”
There is no effective “cure” for intoxication or hangover
Safest rule is to allow 12-24 hours after alcohol consumption, depending on amount of alcohol consumed

## Slide 6: Fatigue and Dehydration
Fatigue and dehydration are of primary concern to glider pilots
  Flights are often conducted in extreme heat and for long duration
Both acute and chronic fatigue can seriously impair pilot performance
  Acute fatigue may be the result of accumulated stress and emotional pressure of a flight
Dehydration can occur very quickly, especially in hot, dry conditions
  3-5 mL/kg/hr or more fluid intake may be required (1-2 liters for a moderate-length flight)
  Deliberate dehydration to avoid urination during flight not recommended

## Slide 7: Hypoxia
Hypoxia (lack of oxygen to the brain) in aviation has two primary causes:
  Carbon monoxide poisoning (mainly for powered aircraft, including motorgliders)
  Altitude
    Altitude reduces the atmospheric pressure, which is what causes oxygen to be absorbed from the lungs to the blood
Effects of hypoxia can be detected as low at 5,000 MSL, but for most healthy individuals effects do not begin to degrade performance until >12,000 MSL
Above 12,000 feet, impairment in judgment, memory, alertness, and decision-making become evident
Above 15,000 feet, tunnel vision and cyanosis may occur
Ability to recognize the problem and take corrective action may be lost after 20-30 minutes at 18,000 feet, and only 5-10 minutes at 20,000 feet
  Unconsciousness follows soon thereafter

## Slide 8: Hyperventilation
Hyperventilation is an abnormal increase in the volume of air breathed in and out of the lungs
Symptoms can include lightheadedness, feeling of suffocation, drowsiness, tingling in extremities
May be caused by stress
Symptoms normally subside within a few minutes after the rate and depth of breathing are consciously brought under control
  Breathing into a paper bag may hasten cessation of symptoms
Hypoxia and hyperventilation can occur at the same time, so if oxygen is available it should be used and the concentration should be set at 100%

## Slide 9: Ear and Sinus Problems
Equalization of pressure in the middle ear is accomplished by air flow through the eustachian tube
Blockage of the eustachian tube will cause an extremely painful buildup in pressure in the middle ear
Causes for blockage include infection and nasal allergies
Similarly, sinus cavities can also become blocked by congestion, leading to extreme pain in the upper cheeks or over the eyes
Both ear and sinus blocks are prevented by not flying with an upper respiratory infection or nasal allergy symptoms
In the event a blockage is not relieved within a few hours of landing, a doctor should be consulted

## Slide 10: Spatial Disorientation
Some types of motions “confuse” the body’s motion sensing system, leading the pilot to “feel” that the aircraft is in a different orientation than it actually is, examples include:
  The leans: Abrupt correction of a banked attitude can result in the illusion of a bank in the opposite direction
  Coriolis illusion: An abrupt head movement while in a constant rate turn can produce the feeling of rotation in a different axis. This is the most overwhelming of all the illusions in flight.
  Graveyard spin: The proper recovery from a developed spin may result in the illusion of a spin in the opposite direction
  Graveyard spiral: Loss of altitude during a prolonged turn may result in the illusion of loss of altitude with wings level. Result will be an ever-tightening spiral.
  Somatogravic illusion: Abrupt acceleration may produce a feeling of being in a nose-up attitude
  Inversion: Abrupt return to straight and level flight from a climb can result in a feeling of tumbling backwards
  Elevator illusion: An abrupt vertical acceleration can result in the illusion of being in a climb
  False Horizon: Certain cloud formations, an obscured horizon, or certain geographic patterns may produce an illusory horizon
  Autokinesis: staring at a point of light for many seconds will make the light appear to be moving around

## Slide 11: Illusions leading to landing errors
Runway width illusion: a narrower than usual runway produces the illusion that the aircraft is higher than it actually is. Result will be a lower approach than normal, possibly striking objects in the approach path
Runway and terrain slope illusion: an upsloping runway or terrain can produce the illusion that the aircraft is higher than it actually is
Featureless terrain illusion: the absence of ground features (e.g. in an approach over snow, water, or in darkness) may produce the illusion that the aircraft is higher than it actually is
Atmospheric illusions: rain or other obscuration may produce the illusion of greater height
Approach lighting illusions: Lights in a straight line (e.g. along a road) may appear to be a runway. Also, bright approach lighting systems may create the illusion of greater distance to the runway. Result will be a higher approach than normal.

## Slide 12: 91.7 Airworthiness
§ 91.7 Civil aircraft airworthiness.
(a) No person may operate a civil aircraft unless it is in an airworthy condition.
(b) The pilot in command of a civil aircraft is responsible for determining whether that aircraft is in condition for safe flight. The pilot in command shall discontinue the flight when unairworthy mechanical, electrical, or structural conditions occur.
Plain English: The PIC is responsible for determining the airworthiness status of the aircraft before flight, and it is a violation of FARs to operate an unairworthy aircraft

## Slide 13: 91.17 Alcohol or drugs
§ 91.17 Alcohol or drugs.
(a) No person may act or attempt to act as a crewmember of a civil aircraft—
(1) Within 8 hours after the consumption of any alcoholic beverage;
(2) While under the influence of alcohol;
(3) While using any drug that affects the person's faculties in any way contrary to safety; or
(4) While having an alcohol concentration of 0.04 or greater in a blood or breath specimen. Alcohol concentration means grams of alcohol per deciliter of blood or grams of alcohol per 210 liters of breath.
(b) Except in an emergency, no pilot of a civil aircraft may allow a person who appears to be intoxicated or who demonstrates by manner or physical indications that the individual is under the influence of drugs (except a medical patient under proper care) to be carried in that aircraft.
(c) A crewmember shall do the following:
(1) On request of a law enforcement officer, submit to a test to indicate the alcohol concentration in the blood or breath, when— …
Plain English: “8 hours from Bottle to Throttle” AND <0.04 BAC. No flying drunks. Must submit to police blood/breath test if requested.

## Slide 14: 91.103 Preflight Action
§ 91.103 Preflight action.
Each pilot in command shall, before beginning a flight, become familiar with all available information concerning that flight. This information must include—
(a) For a flight under IFR or a flight not in the vicinity of an airport, weather reports and forecasts, fuel requirements, alternatives available if the planned flight cannot be completed, and any known traffic delays of which the pilot in command has been advised by ATC;
(b) For any flight, runway lengths at airports of intended use, and the following takeoff and landing distance information:
(1) For civil aircraft for which an approved Airplane or Rotorcraft Flight Manual containing takeoff and landing distance data is required, the takeoff and landing distance data contained therein; and
(2) For civil aircraft other than those specified in paragraph (b)(1) of this section, other reliable information appropriate to the aircraft, relating to aircraft performance under expected values of airport elevation and runway slope, aircraft gross weight, and wind and temperature.
Plain English: PIC must ascertain “all available information” about the flight, including weather, fuel planning, alternates, ATC delays, runway lengths, takeoff and landing distance.

## Slide 15: Effective Visual Scanning
Only a narrow area, called the fovea, in the center of the rear of the eye can send be sharply focused, clear messages to the brain
Objects that are outside of the foveal field will not be clearly communicated to the brain
As a result, the most effective visual scanning technique is a series of short, regularly spaced eye movements that bring successive areas of the sky into the central visual field
  Movements should be no more than 10 degrees apart, and should last at least 1 second
Scanning time must be interspersed with time for in-cockpit chores
  No more than 4-5 seconds of in-cockpit time should be spent for every 16 seconds of scanning for traffic
Pilots must also move their heads around in order to avoid continuous blockage of a portion of the visual field by cockpit structure

## Slide 16: Flight After SCUBA Diving
Flight after SCUBA diving can result in increased risk of decompression sickness (i.e. “the bends”).
  Decompression sickness is caused by gas that has been compressed by underwater pressure coming out of solution in the blood and forming bubbles
In order to avoid decompression sickness, sufficient time must be spent at normal atmospheric pressure to allow dissolved gasses in the blood to return to normal levels before venturing into a lower-pressure (i.e. high altitude) environment.
Recommended waiting times:
  For flight altitudes not exceeding 8,000 feet MSL:
    12 hours after a non-decompression dive
    24 hours after a decompression dive
  For flight above 8,000 feet MSL:
    24 hours regardless of the need for decompression during the dive
  Altitudes are actual flight altitudes, not cabin pressure altitudes, in order to take into consideration the possibility of loss of cabin pressurization during flight.

## Slide 17: Preflight Medical Checklist
I M S A F E
Illness
Medication
Stress
Alcohol
Fatigue
Emotion