## Slide 1: Selected Federal aviation regulations

## Slide 2: General
Part 61- Certification: pilots, flight instructors, and ground instructors
Part 91-General operating and flight rules
NTSB 830-Accident notification

## Slide 3: 61.56 Flight Review
§ 61.56 Flight review.
(a) Except as provided in paragraphs (b) and (f) of this section, a flight review consists of a minimum of 1 hour of flight training and 1 hour of ground training. The review must include:
(1) A review of the current general operating and flight rules of part 91 of this chapter; and
(2) A review of those maneuvers and procedures that, at the discretion of the person giving the review, are necessary for the pilot to demonstrate the safe exercise of the privileges of the pilot certificate.
(b) Glider pilots may substitute a minimum of three instructional flights in a glider, each of which includes a flight to traffic pattern altitude, in lieu of the 1 hour of flight training required in paragraph (a) of this section.
(c) Except as provided in paragraphs (d), (e), and (g) of this section, no person may act as pilot in command of an aircraft unless, since the beginning of the 24th calendar month before the month in which that pilot acts as pilot in command, that person has—
(1) Accomplished a flight review given in an aircraft for which that pilot is rated by an authorized instructor and
(2) A logbook endorsed from an authorized instructor who gave the review certifying that the person has satisfactorily completed the review.

## Slide 4: 61.31 Type rating requirements, additional training, and authorization requirements.
(j) Additional training required for operating a glider. (1) No person may act as pilot in command of a glider—
(i) Using ground-tow procedures, unless that person has satisfactorily accomplished ground and flight training on ground-tow procedures and operations, and has received an endorsement from an authorized instructor who certifies in that pilot's logbook that the pilot has been found proficient in ground-tow procedures and operations;
(ii) Using aerotow procedures, unless that person has satisfactorily accomplished ground and flight training on aerotow procedures and operations, and has received an endorsement from an authorized instructor who certifies in that pilot's logbook that the pilot has been found proficient in aerotow procedures and operations; or
(iii) Using self-launch procedures, unless that person has satisfactorily accomplished ground and flight training on self-launch procedures and operations, and has received an endorsement from an authorized instructor who certifies in that pilot's logbook that the pilot has been found proficient in self-launch procedures and operations.

## Slide 5: 61.57 Recent Flight Experience
§ 61.57 Recent flight experience: Pilot in command.
(a) General experience. (1) Except as provided in paragraph (e) of this section, no person may act as a pilot in command of an aircraft carrying passengers or of an aircraft certificated for more than one pilot flight crewmember unless that person has made at least three takeoffs and three landings within the preceding 90 days, and—
(i) The person acted as the sole manipulator of the flight controls; and
(ii) The required takeoffs and landings were performed in an aircraft of the same category, class, and type (if a type rating is required), and, if the aircraft to be flown is an airplane with a tailwheel, the takeoffs and landings must have been made to a full stop in an airplane with a tailwheel.

## Slide 6: 61.57 Change of Address
§ 61.60 Change of address.
The holder of a pilot, flight instructor, or ground instructor certificate who has made a change in permanent mailing address may not, after 30 days from that date, exercise the privileges of the certificate unless the holder has notified in writing the FAA, Airman Certification Branch, P.O. Box 25082, Oklahoma City, OK 73125, of the new permanent mailing address, or if the permanent mailing address includes a post office box number, then the holder's current residential address.

## Slide 7: Part 61 Subpart C Summary
Subpart C covers student pilots:
  Eligibility Requirements
  Solo Requirements
  Limitations
  Solo X/C requirements
  Operation in Class B, C, D and controlled airports

## Slide 8: Part 61 Subpart D Summary
Subpart D covers recreational pilots:
  Eligibility Requirements
  Aeronautical Knowledge
  Flight proficiency
  Aeronautical experience
  Limitations

## Slide 9: Part 61 Subpart E Summary
Subpart E covers private pilots:
  Eligibility Requirements
  Aeronautical Knowledge
  Flight proficiency
  Aeronautical experience
  Privileges and limitations

## Slide 10: Part 61 Subpart F Summary
Subpart F covers commercial pilots:
  Eligibility Requirements
  Aeronautical Knowledge
  Flight proficiency
  Aeronautical experience
  Privileges and limitations

## Slide 11: Part 61 Subpart J Summary
Subpart J covers sport pilots:
  Eligibility
  Aeronautical knowledge
  Flight proficiency
  Aeronautical experience
  Endorsements
  Privileges and limits

## Slide 12: 91.3 PIC Authority
§ 91.3 Responsibility and authority of the pilot in command.
(a) The pilot in command of an aircraft is directly responsible for, and is the final authority as to, the operation of that aircraft.
(b) In an in-flight emergency requiring immediate action, the pilot in command may deviate from any rule of this part to the extent required to meet that emergency.
(c) Each pilot in command who deviates from a rule under paragraph (b) of this section shall, upon the request of the Administrator, send a written report of that deviation to the Administrator.
Plain English: The PIC is responsible for the operation of the aircraft. In event of emergency, PIC can deviate from any FAR. Written report required IF REQUESTED.

## Slide 13: 91.7 Airworthiness
§ 91.7 Civil aircraft airworthiness.
(a) No person may operate a civil aircraft unless it is in an airworthy condition.
(b) The pilot in command of a civil aircraft is responsible for determining whether that aircraft is in condition for safe flight. The pilot in command shall discontinue the flight when unairworthy mechanical, electrical, or structural conditions occur.
Plain English: The PIC is responsible for determining the airworthiness status of the aircraft before flight, and it is a violation of FARs to operate an unairworthy aircraft

## Slide 14: 91.17 Alcohol or drugs
§ 91.17 Alcohol or drugs.
(a) No person may act or attempt to act as a crewmember of a civil aircraft—
(1) Within 8 hours after the consumption of any alcoholic beverage;
(2) While under the influence of alcohol;
(3) While using any drug that affects the person's faculties in any way contrary to safety; or
(4) While having an alcohol concentration of 0.04 or greater in a blood or breath specimen. Alcohol concentration means grams of alcohol per deciliter of blood or grams of alcohol per 210 liters of breath.
(b) Except in an emergency, no pilot of a civil aircraft may allow a person who appears to be intoxicated or who demonstrates by manner or physical indications that the individual is under the influence of drugs (except a medical patient under proper care) to be carried in that aircraft.
(c) A crewmember shall do the following:
(1) On request of a law enforcement officer, submit to a test to indicate the alcohol concentration in the blood or breath, when— …
Plain English: “8 hours from Bottle to Throttle” AND <0.04 BAC. No flying drunks. Must submit to police blood/breath test if requested.

## Slide 15: 91.103 Preflight Action
§ 91.103 Preflight action.
Each pilot in command shall, before beginning a flight, become familiar with all available information concerning that flight. This information must include—
(a) For a flight under IFR or a flight not in the vicinity of an airport, weather reports and forecasts, fuel requirements, alternatives available if the planned flight cannot be completed, and any known traffic delays of which the pilot in command has been advised by ATC;
(b) For any flight, runway lengths at airports of intended use, and the following takeoff and landing distance information:
(1) For civil aircraft for which an approved Airplane or Rotorcraft Flight Manual containing takeoff and landing distance data is required, the takeoff and landing distance data contained therein; and
(2) For civil aircraft other than those specified in paragraph (b)(1) of this section, other reliable information appropriate to the aircraft, relating to aircraft performance under expected values of airport elevation and runway slope, aircraft gross weight, and wind and temperature.
Plain English: PIC must ascertain “all available information” about the flight, including weather, fuel planning, alternates, ATC delays, runway lengths, takeoff and landing distance.

## Slide 16: 91.125 ATC Light Gun Signals
§ 91.125 ATC light signals.
light signals have the meaning shown in the following table:
Color and type of signal | Meaning with respect to aircraft on surface | Meaning with respect to aircraft in flight
Steady Green | Cleared for takeoff | Cleared to land
Flashing Green | Cleared for taxi | Return for landing (to be followed by steady green at proper time)
Steady Red | Stop | Give way to other aircraft and continue circling
Flashing Red | Taxi clear of runway in use | Airport unsafe-do not land
Flashing White | Return to starting point on airport | Not applicable
Alternating Red/Green | Exercise extreme caution | Exercise extreme caution

## Slide 17: 91.155 Basic VFR Weather Minimums
Class | Visibility | Cloud Clearance
A | N/A-IFR Only | N/A-IFR Only
B | 3 miles | Clear of Clouds
C | 3 miles | 1000 above, 500 below, 2000 horiz.
D | 3 miles | 1000 above, 500 below, 2000 horiz.
E (<10,000 ft. MSL) | 3 miles | 1000 above, 500 below, 2000 horiz.
E (>10,000 ft. MSL) | 5 miles | 1000 above, 1000 below, 1 mile horiz.
G (<1200 AGL, day) | 1 mile | Clear of Clouds
G (>1200 AGL, <10,000 MSL, day) | 3 miles | 1000 above, 500 below, 2000 horiz.
G (>10,000 MSL, day or night) | 5 miles | 1000 above, 1000 below, 1 mile horiz.
G (<10,000 MSL, night) | 3 miles | 1000 above, 500 below, 2000 horiz.
Notes: Summary only, check regs for actual chart, miles are statute miles

## Slide 18: 91.211 Supplemental Oxygen
§ 91.211 Supplemental oxygen.
(a) General. No person may operate a civil aircraft of U.S. registry—
(1) At cabin pressure altitudes above 12,500 feet (MSL) up to and including 14,000 feet (MSL) unless the required minimum flight crew is provided with and uses supplemental oxygen for that part of the flight at those altitudes that is of more than 30 minutes duration;
(2) At cabin pressure altitudes above 14,000 feet (MSL) unless the required minimum flight crew is provided with and uses supplemental oxygen during the entire flight time at those altitudes; and
(3) At cabin pressure altitudes above 15,000 feet (MSL) unless each occupant of the aircraft is provided with supplemental oxygen.
Plain English: If above 12,500 feet for more than 30 minutes, pilot must use oxygen. Above 14,000 feet for any length of time, pilot must use oxygen. Above 15,000 feel, passengers must be provided with oxygen.

## Slide 19: 91.215 ATC transponder and altitude reporting equipment and use.
Summary:
  Gliders (without electrical systems) are generally exempt from transponder requirements, even in the “mode C veil” within 30 nm of a Class B or C airport, EXCEPT:
    Cannot fly into Class A, B, or C airspace
    Cannot fly > 10,000 ft. MSL within mode C veil
    Cannot fly > ceiling of class B or C within the veil
    Cannot overfly class B or C airspace

## Slide 20: 91.303 Aerobatic flight.
§ 91.303 Aerobatic flight.
No person may operate an aircraft in aerobatic flight—
(a) Over any congested area of a city, town, or settlement;
(b) Over an open air assembly of persons;
(c) Within the lateral boundaries of the surface areas of Class B, Class C, Class D, or Class E airspace designated for an airport;
(d) Within 4 nautical miles of the center line of any Federal airway;
(e) Below an altitude of 1,500 feet above the surface; or
(f) When flight visibility is less than 3 statute miles.
For the purposes of this section, aerobatic flight means an intentional maneuver involving an abrupt change in an aircraft's attitude, an abnormal attitude, or abnormal acceleration, not necessary for normal flight.

## Slide 21: NTSB 830-Definitions
Accident: an occurrence associated with the operation of an aircraft which takes place between the time any person boards the aircraft with the intention of flight and all such persons have disembarked, and in which any person suffers death or serious injury, or in which the aircraft receives substantial damage
Serious Injury: any injury which: (1) Requires hospitalization for more than 48 hours, commencing within 7 days from the date of the injury was received; (2) results in a fracture of any bone (except simple fractures of fingers, toes, or nose); (3) causes severe hemorrhages, nerve, muscle, or tendon damage; (4) involves any internal organ; or (5) involves second- or third-degree burns, or any burns affecting more than 5 percent of the body surface.
Substantial Damage: damage or failure which adversely affects the structural strength, performance, or flight characteristics of the aircraft, and which would normally require major repair or replacement of the affected component. Engine failure or damage limited to an engine if only one engine fails or is damaged, bent fairings or cowling, dented skin, small punctured holes in the skin or fabric, ground damage to rotor or propeller blades, and damage to landing gear, wheels, tires, flaps, engine accessories, brakes, or wingtips are not considered “substantial damage” for the purpose of this part.

## Slide 22: NTSB 830-Requirements
NTSB must be notified immediately in the event of an accident OR any of the following incidents:
  Flight control system malfunction or failure;
  Inability of any required flight crewmember to perform normal flight duties as a result of injury or illness;
  Failure of structural components of a turbine engine excluding compressor and turbine blades and vanes;
  In-flight fire; or
  Aircraft collide in flight.
  Damage to property, other than the aircraft, estimated to exceed $25,000 for repair (including materials and labor) or fair market value in the event of total loss, whichever is less
  Additional requirements apply to large multiengine aircraft
Wreckage, cargo, mail, and records related to the aircraft and crew must be preserved
A report, including a statement for each crewmember, must be filed with the NTSB within 10 days of an accident. Incidents that require immediate reporting do not require an NTSB report unless requested.

## Slide 23: NTSB Notification
NTSB Notification: P-FACTION Property damage more than $25,000 Fire, in flight Accident Collision, in flight Turbine failure Illness of crew member Overdue aircraft No control: control failure of any sort